Small Home Level A Floor Plan Mark Sheet         Name: ___________________

Bold red items are related to the modified plan and affects marks			Block: _________

| ( | ( Check off if completed and have some other student check your work. |
| --- | --- |
|  | AutoCad Floor Plan Mark Sheet | (Out of) | Mark |
|  | Walls - exterior (6”), interior (4”) Walls trimmed at each corner and joining wall. | 10 |  |
|  | Windows At least one in each bedroom (minimum 4’ total combined – need) Sizes in 1’ increments (2’, 3’, 4’, 5’, etc.) Windows do not overlap inside cabinets or shower | 5 |  |
|  | Doors 3’ outside with sill plate (2” out and 2” over) 2’-6” inside doors At least 3- 4” of wall on each side of the door Walls are trimmed on all doors. | 5 |  |
|  | Closets - doors, shelves (16”) and rods (back 2” and hidden line) At least one per bedroom (minimum 3 feet wide), depth A coat closet near entrance (minimum 3 feet wide) A linen closet in or near bathroom(s) - no rod and shelf wider (full depth) Recommend a broom closet with a depth of 2’-4” or 2’-0” If walk-in closet: Min. 4' deep & min. 5' wide for 1-sided shelf or 6' wide for 2-sided. | 5 |  |
|  | Bathroom - counter (18”-24” wide), sink, tub, shower, and toilet | 5 |  |
|  | Kitchen – counter (24”), top cupboards (12” – hidden line) and appliances 3 feet walking space around island (if island added) | 10 |  |
|  | Roof Line - drawn in phantom line | 5 |  |
|  | Dimensions - outside ***numbers read from bottom and right side*** 1st dimension line - center of windows/doors and to outside of exterior walls 2nd dimension line - center of interior walls and to outside of exterior walls 3rd dimension line - outside of exterior walls 4th dimension line - overall size (outside to outside of furthest exterior walls) | 15 |  |
|  | Dimensions - interior ***do not dimension interior doors*** Inside horizontal and vertical dimension line(s) to pick up any interior walls not dimensioned outside (outside of exterior walls and center of interior walls) | 5 |  |
|  | Electrical Lights for each room and hallways Switches for lights and attached with double curved center or hidden lines. 3 way switches for stairways (top and bottom) and where appropriate Outlets - 30” from corner of room and every 12’ and every 6’ on counters 220 outlets for stove/oven and dryer GFI outlet for bathroom and GFI/WP outlet for front and back exterior | 15 |  |
|  | Labeling Rooms & closets - labeled in proper lettering (all capitals) Viewport layer turned off | 5 |  |
|  | BONUS: LAYOUT SPACE WITH TITLE BLOCK VIEWPORT LAYER TURNED OFF CUSTOM SCALE: 4" = Paper Unit : 12" Drawing Units | 10 |  |
|  | Total = | 85 |  |

Note: Print off, fill out and staple to the top left corner of the front of your floorplan, then submit to the marking

table – see your teacher.

Elevations Mark Sheet

# Name: _______________  Block:____

|  | ( Check off if completed and have some other student check your work. |
| --- | --- |
|  | Elevations | Value (Out of) | Mark |
|  | Walls / Doors / Windows / Chimney ’ wall height (with eaves trough will be 6" higher) Accurate to the floor plan (lines up) Doors 7” high and 3’ wide Top of windows lined up to top of doors | /20 5 for each elevation |  |
|  | Roof pitch, matching roof heights and roof overhang Standard 4/12, 5/12, 6/12, 7/12 etc. 12 Roof pitch(es) indicated and about this size on each elevation ( 5 Check the roof is the same height from one elevation to the next Overhang 6” to 2’ - comes from top of 8’ wall and 6” up then out Accurate to floor plan | /16 4 for each elevation |  |
|  | Dimensions Ground to top of the eaves (top of the overhang) To all roof peaks on all elevations To all parts of a bay window on all elevations To special detail (ex, brick, chimney, etc) Over hang | /16 4 for each elevation |  |
|  | Rendered / Title block and border Hatch - Stucco, siding, shingles, bricks, etc. Labels as to the materials (use proper names - stucco, siding, shingles, bricks Label under each elevation --- text height about 12 inches (FRONT ELEVATION, BACK ELEVATION, RIGHT ELEVATION, etc.) Your name, title of drawing, block, scale, etc. | /12 3 for each elevation |  |
|  | Difficulty of plan 0 if no or little change from the basic plan 8 if easy - basic rectangle, one jut out and simple roof 12 if medium - rectangle with some jutting out parts and intersecting roof line 16 if hard - complicated layout, complicated roof, bay windows, etc. | /16 4 for each elevation |  |
|  | Penalties -5 if scale (1/4”=1’) is incorrect -5 if linetype is not continuous and all lines in black except the windows and doors (no colour needed) | -10 |  |
|  | All Elevations Total = | /80 |  |

Note: Submit your FLOOR PLAN with your ELEVATIONS

Note: Fill out, print off and staple to the top left corner of the front of your elevations, then submit to the marking table – see your teacher.

# Text boxes

Exterior side